## Slide 1: Drinking-water Treatment
Feng “Frank” Xiao,
Department of Civil Engineering,
University of North Dakota
NATURE Sunday Academy Workshop (July 24)

## Slide 2
=
Treatment
Source
Water
+
Contaminants:
Particles (clay, silt)
Natural organic matter
Microcontaminants
(e.g., pharmaceuticals)
Bacteria
Virus
Tap Water
Surface water
or groundwater
2

## Slide 3
Distribution system
Drinking-water Treatment
Intake
Sedimentation
Coagulation
Storage
Filtration
Disinfection
Source
Water
Particles (clay, silt)
Natural organic matter
Microcontaminants
Bacteria
Virus
Low turbidity
High turbidity
Drinking water standard:
Turbidity ≤ 0.3 NTU at least 95% of samples in any month
Goal of coagulation: Reducing turbidity
Notes: Nephelometric ([,nefilə'metrik]) Turbidity Unit

## Slide 4
Induce Particle Aggregation
Coagulation
4
Goal: Reducing turbidity
Coagulation
Aggregates
(flocs)
Particles
Why?
Induced
aggregation
Notes: Goal

## Slide 5
Stokes’ Law
George Stokes
1819–1903
R: radius of the particles (in m)
: particle’s settling velocity (m/s)
g: gravitational acceleration (m/s2)
: mass density of particles (kg/m3)
: mass density of water (kg/m3)
: dynamic viscosity of water (kg/m/s)
5

## Slide 6
Particle Size versus Settling Time
Particle Size
mm
Order of Size
Time to Settle
for 1 m
0.00001 | Colloidal | >50 Years
0.0001 | Colloidal | 9 year
0.001 | Bacteria | 32 days
0.01 | Silt | 8 hours
0.1 | Fine Sand | 5 min
1.0 | Coarse Sand | 9 Seconds
6

## Slide 7
Induce Particle Aggregation
Coagulation
7
Goal: Reducing turbidity
Coagulation
Aggregates
(flocs)
Particles
How?
Notes: Goal

## Slide 8
* Fine Suspended Particles Have an Electrostatic Charge (Usually –)
Charge Neutralization
(encourage contact and aggregation)
* Floc Enmeshment
Electrostatic repulsion
keeps particles apart
Like charges repel
Mechanisms of
Coagulation
flocs
Al3+; Fe3+ (coagulants)
8

## Slide 9: Coagulant
Aluminum Sulfate (Al2(SO4)318H2O) (alum)
Ferric Chloride (Fe3+)
Metal Salts
Such As
9
(drinking water)
(wastewater)

## Slide 10: Coagulation Process
Rapid Mixing (adequate contact)
(~1 min)
Slow Mixing (floc formation)
(Flocculation)
(~20 min)
3. Settling (~30 min)
Coagulants (Al3+; Fe3+)
flocs
10
Notes: ['frædʒəl] Operation details of coagulation
, gentelly

## Slide 11: PROCESS CONTROL
1. Provide complete rapid mixing.
2. Control slow mixing for floc.
11
G is the velocity gradient (sec–1)
P is the power input (kW)
μ is the viscosity of the water
and V is the volume of the system (tank)

## Slide 12: PROCESS CONTROL
1. Provide complete rapid mixing.
2. Control slow mixing for floc.
3. Control coagulant dose.
12
(jar test)

## Slide 13
Jar Tests
A laboratory procedure to determine the optimum coagulant dose
Simulates the coagulation process
Jar test set-up
13
jar
stir
flocs
Adjusting mixing rate

## Slide 14
After jar test (coagulation),
Turn off the mixers and allow
flocs to settle for 30 min
Measure the final residual
turbidity in each jar
Plot residual turbidity against coagulant dosage
14
Chart: Coagulant Dosage (mg/L)
| 2.5 | 4.5999999999999996 | 6.7 | 9.1 | 11.2 | 12 | 15.6 | 20.8 | 30.8 | 41.5 | 60.5 | 70.7 | 80
 | 16 | 15 | 13.8 | 11.6 | 9.8 | 7.6 | 5 | 3.1 | 2.9 | 2.6 | 2.6 | 3.1 | 3.3
Optimum coagulant dosage

## Slide 15
Induce Particle Aggregation
Coagulation
15
Goal: Reducing turbidity
Coagulation
Aggregates
(flocs)
Particles
Al3+; Fe3+ (coagulants)
Notes: In summary,

## Slide 16: Treatment Process
Rapid Mixing
Slow Mixing
Settling
Coagulation
flocs
Al3+; Fe3+ (coagulants)
16

## Slide 17
Less Solids and Natural Organic Matter
Less Disinfection Byproducts
Coagulation
Outcome
17
Notes: Disinfection, talk it in next class.

## Slide 18
i) Understand the fundamentals of coagulation/flocculation
Lesson Objectives
18
Notes: Goal

## Slide 19
ii) develop analytical skills by participating in a bench-scale water treatment experiment
Lesson Objectives
19
Notes: Goal

## Slide 20
iii) identify safe operational procedures, sampling, and laboratory testing techniques
Lesson Objectives
20
Notes: Goal

## Slide 21
Overall Goal:
To illustrate some basic principles of water treatment that involves the removal of particulate matter.
Activity:
Coagulation Jar Tests
21
Notes: Goal

## Slide 22
Turbidity: The cloudiness of water, caused by suspended particles scattering light, is called turbidity.
pH: pH is a term used to express the concentration of the acid or alkaline condition of a solution.
Activity:
Coagulation Jar Tests
22
Notes: Goal

## Slide 23
Measure the turbidity and pH of suspension. Number and fill six jars with the prepared suspension.
Place the 6 jars under the mechanical stirrer and turn on the motor. Immediately adjust the speed to 140 rpm (before coagulant is added).
Using pipettes, add alum stock solution to the six jars at the following dosages (see Table 1).
Maintain the mechanical stirrer at 140 rpm for 1 minute, then reduce to 30 rpm. Stir at this rate for 15 more minutes. Observe the jars carefully and record the time at which the floc appears in each jar. Floc may be very small, but will appear as discretely visible particles.
At the end of the slow stirring period, stop the stirrer.
Activity #1

## Slide 24
5. After settling, during which time the jars should not be disturbed, pipette out sufficient supernatant and test it for pH and turbidity.
6. Report the data collected (Table 2).
7. Construct one graph (#1) by plotting the turbidity data (NTU) versus alum dosage (mg/L); including the raw water point (0 mg/L alum dosage) into this graph.
8. Find the optimum alum dosage.
9. Construct another graph (#2) by plotting the water pH as a function of alum dosage (mg/L).
10. Construct the third graph (#3) by plotting the time of floc formation (min) as a function alum dosage. Are there any similarities between Graphs #1 and #3?
Activity #2

## Slide 25
Appendix

## Slide 26
Questions?