## Slide 1: Smart “PIGs” in Pipes
Dr. Ying Huang, Associate Professor
Shuomang Shi, Ph. D student
Department of Civil & Environmental Engineering, NDSU

## Slide 2: Introduction of Pipes
Pipe transports:
Water to each household (Material made: PVC, steel)
Wastewater to the wastewater treatment plant (sewer pipe) (Material made: PVC, steel)
Chemicals to the farm and needed business (Material made: PVC, steel)
Other liquids (Material made: steel)
* Photos are obtained from Google, the copy rights of the photos retain to the original sites

## Slide 3: Introduction of Pipe Health Conditions
Mechanical force induced damages such as scratches, cracks, dents, disbonded coating, holes, etc.
Chemical reaction induced damages such as corrosion and erosion
Very important to inspect the pipe timely to ensure their safety
* Photos are obtained from Google, the copy rights of the photos retain to the original sites

## Slide 4: Introduction of PIGs
What it is a PIG?
  Smart PIG --- pipe cleaning, dewatering, and inspection tool
Why is it called a smart pig?
  The term ‘pig’ came about in two different ways. The original pipe pigs of straw wrapped in wire made a squealing noise as they moved down the Pipe. They sounded like a pig. The other is an acronym for Pipe Inspection Gauge (PIG).
Types and Functions of PIGs:
  Cleaning long-term wax and dirt
  Observing of the working condition of inner-pipe walls
  Locating and initiate analysis of defects with embedded sensors

## Slide 5: Introduction of PIGs
Composition of PIGs
  Main body (main axis)
  Cleaning disc (rubber plates)
  Motion unite (Thrust motor/Pressure)
  Attached sensors (camera, acoustic, optical)Watch a video: 5 minutes
Watch a video to learn more:
  http://news.mit.edu/2017/robot-finds-leaks-water-pipes-0718
  https://www.youtube.com/watch?v=H7PIjp2exik
This project focuses on the use of a Camera PIG!
  https://www.youtube.com/watch?v=irK5MOs4HQc
* Photos are obtained from Google, the copy rights of the photos retain to the original sites

## Slide 6: Goals of the Activity
Goals of this activity:
- Learn how pipes work for transporting water, and wastewater, etc.;
- Explore typical damages pipes suffer under practical use conditions;
- Understand smart pig and why smart pigs are needed;
- Identify how smart pigs work for pipe inspection;
- Demonstrate how to use the technologies in smart PIG to locate damage
- Explore how to maintain a pipes in a good health condition.

## Slide 7: Vocabulary Taboo Game
Notes: Pipe: A pipe is a tubular section or hollow cylinder, usually but not necessarily of circular cross-section used mainly to convey substances which can flow such as liquids and gases (fluids), slurries, powders, and masses of small solids. It can also be used for structural applications; hollow pipe is far stiffer per unit weight than solid members.
Pipe applications: Pipes can be used to transport water supply, waste water, chemical, energy related fluids, etc.
Pipe materials: Steel and other metals, Plastic such as PVC, Concrete, etc.
Pipe smart PIGs: acronym for Pipeline Inspection Gauge is a robot of sorts that helps pipeline companies identify potential problems before they happen or to pinpoint pipe damage and issues.

## Slide 8: Fact Sheet 1
Review the factsheet and answer the questions to learn fun facts about pipes and smart PIGs.

## Slide 9: Questions
1. Does cleaning pigs perform inspection?
    Yes; B. No
2. What materials can pipes be made of?
A. Paper; B. Steel; C. PVC.

## Slide 10: Fact Sheet 2
Review the factsheet and answer the questions to learn fun facts about pipe damage.

## Slide 11: Questions
Is corrosion a geometrical defect?
A. Yes B. No
2. The damages on pipes can be ignored with no consequences?
A. Yes B. No

## Slide 12: Safety Rules
For sandpaper, be careful not to rub abrasively on skin.
For acetone, use only a small amount and use a wrap to put the acetone on the surface of pipe, also avoid direct contact of acetone on skin, eyes, mouth, etc.
For electrical drills, remove the drill heads when not using and do not face the drill head close to hands, face, or any body parts.

## Slide 13: Damage Activity– Set up
1) Divide the class into groups of four.
2) Each team needs to create a team name and display on index card.
3) Select one size of pipe and matching fittings.
  Each team needs two 2-ft pipes and one fitting.
4) Use the pictures on the following slides to see what types of damages can be made to your pipes.
  Damage 1: Sandpaper
  Damage 2: Drill
  Damage 3: Acetone

## Slide 14: Damage Activity– Damage 1
Use sandpaper to make damage type #1.
Select 1 grade of sandpaper from different grades (extra course, course, medium course, fine, extra fine). Then sand the inner-surface of PVC pips to make rough surface area. Use the washable paint to mark the damage as #1.

## Slide 15: Damage Activity– Damage 2
Use Electrical drill to make damage type #2.
Select a drill head from the models available, assemble the drill, and make small holes through pipe walls. Then use the washable paint to mark the damage as #2.

## Slide 16: Damage Activity– Damage 3
Use Acetone to make chemical reaction on PVC pipe for damage #3
Dip a piece of paper towel into acetone solvent and then place it on the inner-surface of PVC pipes. Let stand for at least 10min to make complete reaction when obvious grains appear. Then use the washable paint to mark the damage as #3.

## Slide 17: Fact Sheet 3
Review the factsheet and answer the questions to learn fun facts about technology used to inspect pipes.

## Slide 18: Questions
Is the smart inspection pig able to identify cracks in pipes?
A. Yes B. No.
2. Any other inspection technologies you can think of which can be used for pipe inspection?

## Slide 19: DIY Robot
Using the instructions found within the robot kits or by searching for “how-to” videos, construct the robot provided by your teacher.
SunFounder Smart Video Car Kit V2.0 PiCar-v

## Slide 20: Document Damage
Install the camera
Adjust the camera positions to best picture taken inside pipes.
Documenting the locations, size, and types of damages made on pipes using the Document Damage Graphic Organizer.

## Slide 21: Review Ten Word Summaries

## Slide 22: Fact Sheet 4
Review the factsheet and answer the questions to learn fun facts about pipe maintenance according to different damages

## Slide 23: Questions
Pipes are always maintained in a preventive way?
A. Yes B. No.
2. What maintenance approach will you use if you are an engineer manage the water pipes?

## Slide 24: Acknowledgments
Grant#: CMMI-1750316
Grant#: 693JK31850008CAAP

## Slide 25: Questions?
Contact:
Dr. Ying Huang, Civil and Environmental Engineering Department, North Dakota State University (contact email: ying.huang@ndsu.edu, CIE201F, NDSU.);
Shuomang Shi (Ph. D. student at NDSU, shuomang.shi@ndsu.edu) .